## Slide 2: What is the ChapR?
A remote for controlling FTC robots without a PC
Small, portable device with 2 USB connectors for the joysticks
A device to release waitForStart() on any program running on the brick

## Slide 3: Features
Pocket-size
2 USB connectors for the joysticks
waitForStart() release
Connects to the last known NXT brick upon boot

## Slide 4: Giving Back to the Community
Allow less fortunate teams to demo, test and practice driving without needing multiple PCs
The profits made will be used to give ChapRs to teams in need (every 1 in 4 or 1 in 5 ChapRs will be free)

## Slide 5: What do we need?
Someone to accept money from the website
A 501c3 non-profit organization to accept money and assure people that they won’t have to pay taxes
An organization to order parts and store excess profits that will go toward giving out free ChapRs

## Slide 6: Design - Case
3D printed

## Slide 7: Design - Hardware
Arduino Mini
VDIP (2 USB ports which receive joystick input)
LEDs (one red and one blue)
Speaker (to transmit information to the user)
Button (to make the ChapR bluetooth discoverable or release a waitForStart)
Bluetooth module (which sends the joystick input to the NXT)

## Slide 8: Design - Software
Runs on the Arduino Mini
lowPower mode
  Entered when the ChapR receives no joystick information for a period of time
  Doesn’t transmit via Bluetooth, but resumes normal function upon joystick input
zombieMode
  Entered when the ChapR receives no data for a long period of time
  Shuts down entirely and must be rebooted

## Slide 9: Timeline

## Slide 10: Promotion
FTC World Championships
  Assessed interest level (8.5 out of 10)
  Tested the prototype (1st time connection needed work, but worked beautifully from then on)
Commercial
  Highlights problems without the ChapR (in 3 scenarios)
  Explains how the ChapR solves each
  Demoes the ChapR

## Slide 11: Future Promotion
Outtakes
  Comedic relief on the website/youtube channel of our attempts to make a commercial
“Appisodes”
  Scenarios where the ChapR is needed (and/or comes in to save the day)
Australia
  Sending a prototype to the Asia Pacific Qualifier for some overseas exposure