## Slide 1
WHAT IS
?

## Slide 3: Features
With
Akshay Prakash

## Slide 4: Driving
Plug in joysticks
Hit the action button if needed
Hold power button to turn on
Select program
1.
2.
3.
4.

## Slide 5: The Kill Switch
Tap power button to abort program
TAP
HOLD
Hold power button to turn off ChapR

## Slide 6: Pairing
Via Bluetooth
Hold down both buttons on the ChapR
Use NXT menus to find the ChapR and connect with it

## Slide 7: Pairing Continued
Via USB
Make sure Bluetooth is on
Plug in the cable

## Slide 8: Configurable
name - the name of the ChapR
timeout - the time before the ChapR turns itself off
lag - the time between sending messages
mode - tele-op or autonomous
personality - the compatibility of the ChapR with various “flavors” of programs
  NXT-RobotC
  NXT-G
  NXT-LabView
Configurable via flash drive or serial port

## Slide 9: Tele-Op Remote Start
In progress!
Implementing the ability to start the program from afar using the action button
Uses the program that has been loaded into Program Chooser

## Slide 10: Programmable
The programmer and code on our website can be used to reprogram the ChapR

## Slide 11: Hardware
With
Ben Gorr

## Slide 12: History of Hardware – starting with the NXT Remote!

## Slide 13: first ChapR made of shield

## Slide 14: v0.2 – condensed design!

## Slide 15: v0.3 – Updated case and Board!

## Slide 16: v1.0 – Release version!
Arduino Pro-Mini
RN-42
VDIP

## Slide 17
Port 1
Port 2
USB Interface (VDIP)
Bluetooth Transmitter (RN-42)
Microprocessor (Arduino Pro-Mini)
Joystick Data
BT Packets
Connected?

## Slide 18: Manufacturing Process
PCB done in Eagle and manufactured by Futurlec.
We receive the board, then solder the parts in place and manufacture case.
Case is modified off-the-shelf unit.
Board manufacturing process takes 1 hour 30 minutes!
If orders start becoming too much to handle we may outsource production, but for now we enjoy building them ourselves.

## Slide 19: Software
With
Rachel Gardner

## Slide 20: The Software
Arduino Sketch written in C
Versioned using an EEPROM (local memory on the Arduino) “magic string”
Managed using an SVN
22 subclasses
Check out www.TheChapR.com/build-your-own to see the actual copy

## Slide 21
Set Up
Power Up
Initialize Bluetooth
Initialize VDIP
Read EEPROM
Check for device in VDIP
Configure EEPROM
Grab joystick packets
Connect to NXT
If USB
If joystick
If NXT
Lag is added
Check EEPROM
Checks inactivity
If greater than timeout
Power off ChapR
Checks if Serial is available
If available
Check buttons
If PWR
If WFS
Kill switch
Release WFS
Turn off
tapped
held
Check connection
If BT connected
Send data to NXT
Check personality

## Slide 22: Business Model
With
Rachel Gardner

## Slide 23: Moving Forward
Selling each for $100 with a production cost of $75
Shipping out one charity ChapR for every 3 sold
All production is done by Westlake high school students volunteering their time
We’re building as fast as we can

## Slide 24: Moving Forward
WESTA is our 501(c)3 non-profit organization
Working on filing a patent
Chap Robotics is trying to give back to the FIRST community
Learned marketing, software, hardware, manufacturing and design.
www.TheChapR.com has support systems for using the ChapR

## Slide 25: Questions? Feedback?
Any ways to spread the word?
Advice for manufacturing or production?
General feedback?
Uses we didn’t think of?
See www.TheChapR.com to get more information, donate or order!